Hovercraft protocol

Table of content

1. Change history
2. Document purpose
3. Hovercraft protocol

Change history

25/03 : The first version of the document containing the prototype of communication protocol is created. This document will be presented in the test and integration meeting on 26/03 to get some feedbacks.

Hovercraft protocol

Fan forward speed:	3bits 111 = 7	110=6	101=5	…
With 3 bits, we can cover form 0 to 7

Fan hovering speed:	2bits 11 = 3	10 = 2	01 = 1	00=off
With 2 bits, we can cover from 0 to 3

Ruder Direction:	2bits	11= Left	10= Right	01=Straight forward
With 2 bits, we can cover left, right, and straight
Hovercraft Speed:	4bits	1111= 15	1110=14	1101=13	…
with 4 bits, we can cover the speed of 0 to 16 (I think this would be the maximum speed...)

Hovercraft Pressure: 2bits	11= high	10= normal	01= low	00=off
with 2 bits, we can cover 4 levels ( high, normal, low, off )

Battery level: 2 bits	11= 3 (full)	…	000= 0 (empty)

First Scenario:

Fan forward speed: off
Fan hovering speed: off
Ruder direction: left

1. The number 58 is sent by PC part ( The number range is 0 – 255 )
2. On hovercraft, one binary is received ( 58 or in binary 00110110 )
  The binary would be considered as following picture:

Fan forward speed
Fan hovering speed
Ruder Direction

0	0	1	1	0	1	1	0

1. The following information will be discovered by parsing the binary:
  1. The fan forward speed is : 6
  2. Fan hovering speed is: 2 (normal)
  3. Ruder direction: 1 (straight forward)

The following binaries will be sent back to the PC as a result:

Fan hovering speed

Fan forward speed
Ruder Direction
Hovercraft Pressure
Battery level

Hovercraft Speed

1	0	1	0	1	1	1	0	0	0	1	1	0	1	1	0